## Slide 1: The Electricity Sector in Mozambique
[March 2015]
[Amilcar Cipriano & Colin Waugh]
An Analysis of the Power Crisis and its Impact on the Business Environment

## Slide 2
Summary
Underplanning for Growth
Policy focus on Grid Extension
Generation, maintenance, transmission lagging:
Load Shedding, Blackouts
Urgent need for diversification, infrastructure
27% Administration, T & D Losses
Uneconomic tariff for Investors

## Slide 3: Study Goals
Raise public awareness of:
The national energy deficit
The challenge of meeting growing demand ahead of a rapid development phase in the natural resources sector.
Contribute to the discourse around:
The role of the State; the need to stimulate investment
Suggesting policy measures for urgent implementation

## Slide 4: Mozambican National Electric Power Network: Medium Load forecast: Medium Load forecast

## Slide 5: Statement of the Problem
Load exceeds available capacity, giving rise to excess power imports, from SAPP, IPPs at cost in excess of tariff
Urgent need to promote the construction of additional and alternative sources of power to create transmission infrastructures and
Deliver power to load centers with cost effective rates
Implement measures aimed at stimulating new investment, achieving efficient supply.

## Slide 6: Electricity Supply 2013: Dominance of HCB
CLICK TO ADD BREAKER SLIDE TITLE
Chart: 2013-Electricity supply
| Hydro EDM | Thermal EDM | Thermal IPP | Imports | Hydro HCB
 | 222 | 29 | 95 | 109 | 4084

## Slide 7: Evolution of the Power Matrix
Commercial operation of HCB – began 1975 contributing significantly to the load up to 1981 when war disrupted generation
EDM thermal generation gradually diminished while imports dominated until 1992 Peace Accords
Only in 2012 came the construction at Gigawatt Park/AGGREKO in the Ressano Garcia area

## Slide 8: Cumulative Consumption by Source, 1955-2012
Chart: Cumulative Consumption by Source [GWh]
| 1955 | 1956 | 1957 | 1958 | 1959 | 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
Hydro [EDM] | 10 | 10 | 20 | 25 | 40 | 50 | 55 | 50 | 52 | 57 | 60 | 75 | 75 | 73 | 100 | 140 | 150 | 180 | 205 | 207 | 200 | 175 | 170 | 175 | 175 | 160 | 155 | 148 | 138 | 144 | 95 | 90 | 125 | 100 | 150 | 150 | 175 | 180 | 175 | 165 | 183 | 209 | 185 | 207 | 266 | 255 | 258 | 263 | 243 | 109 | 158 | 219 | 216 | 341 | 375 | 350 | 367.23 | 239.6 | 222.04
IPP | 0 | 29.64 | 94.6
Thermal [EdM] | 50 | 65 | 76 | 75 | 100 | 100 | 140 | 150 | 163 | 183 | 215 | 225 | 250 | 277 | 295 | 295 | 345 | 360 | 285 | 223 | 200 | 215 | 220 | 155 | 135 | 125 | 165 | 147 | 172 | 146 | 185 | 110 | 155 | 155 | 192 | 172 | 151 | 94 | 49 | 35 | 29 | 30 | 33 | 36 | 36 | 42 | 43 | 34 | 34 | 39 | 15 | 6 | 7 | 11 | 12 | 17.71 | 22.03 | 23.61 | 29.05
Imports | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 150 | 225 | 200 | 170 | 170 | 90 | 100 | 55 | 260 | 300 | 290 | 300 | 220 | 300 | 320 | 345 | 307 | 322 | 373 | 436 | 511 | 567 | 601 | 599 | 686 | 343 | 73 | 243 | 33 | 13 | 11 | 14 | 19 | 27 | 17 | 27 | 32 | 67.43 | 86.48 | 84.1 | 108.74
Hydro HCB | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 172 | 185 | 265 | 45 | 40 | 45 | 40 | 40 | 40 | 25 | 55 | 93 | 94 | 99 | 95 | 118 | 141 | 152 | 186 | 207 | 616 | 953 | 854 | 1138 | 1387 | 1543 | 1765 | 1905 | 2129 | 2381 | 2653 | 2775 | 3118.18 | 3549.04 | 3873.6 | 4083.89

## Slide 9: Future Generation Projects
New supply from the north continues to exploit Hydropower (Mphanda Nkuwa, Cahora Bassa, Lurio etc)
Coal will continue to play a role in the centre: Moatize, Benga, Nkondezi
Thermal Power burning natural gas will play a major role in the south (Maputo and Ressano Garcia areas)

## Slide 10: Generation projects (Hydro & thermal) by location

## Slide 11: Generation projects under implementation

## Slide 12: Projects Proposed and Underway
Chicamba and Mavuzi Power plants rehabilitation
Reinforcement of several substations in the Northern grid
New 275 KV line from Ressano Garcia to Macia
New 400 KV from Caia do Namialo

## Slide 13: International Initiatives
Kenya: partial public sale of shares in KenGen, national power gen company
By 2013 seven IPPs generating 20% of total
Nigeria: Grid only delivering 5 GW in 2013 to country of 170m; 25GW private generation
Major overhaul of industry: most generation and distribution privatized, heavy local banking sector support; bottlenecks persist

## Slide 14: Discussion & Analysis
Slow pace of regulatory, legislative reform
Heavy price paid for policy of subsidized universal tariff, ignoring cost-benefit basis
Unbundling of ownership, management of Generation and Distribution – PPAs
Accelerated Development Zones: flexible adoption of existing incentive mechanisms

## Slide 15: Concentration of Energy Supply by Source

## Slide 16: Conclusion and Recommendations
More flexible application of regulations in place, stimulation of incentive to invest
Enhanced measures to combat network losses
Unbundling with extension of IPP generation including mini-grid PPP distribution
Tariff application based on greater cost-benefit assessment
short term outsourcing of transmission O &M